## Slide 1
Flood Risk Modelling
using
flood hazard & vulnerability factors
Modelling of the MMR Region in Maharashtra, India
Presented by
Brahad - 2021112004
Manasa - 2022101131

## Slide 2
MMR Region of Maharashtra
  High Population Density and Urbanization: rapid urbanization has led to significant land use changes, reducing natural drainage areas and increasing impermeable surfaces
  Monsoon Season Intensity: receives heavy rainfall during the monsoon season, often leading to waterlogging
  Climate Change Impact: 2017 floods (heaviest rains in a decade) attributed to global warming
  Economic Importance: Mumbai is a major economic center
Region of Interest
Choosing our
Why?

## Slide 3
Shapefiles containing the region of interest

## Slide 4
  Rainfall
  Elevation
  Slope
  Distance from Rivers
  Drainage Density
  Topological Wetness Index (TWI)
  Land Use Land Cover (LULC)
  Socio-Economic Factors
Factors Analyzed & Assessed
Flood Risk
Quantifying

## Slide 5
Rainfall in the MMR
The Rainfall map was modelled on QGIS using the Spatial Interpolation (IDW) Technique
Data was collected from the CHRS Data Portal for the 5 districts in the MMR: Raigad (Partial), Palghar (Partial), Thane, Mumbai Suburban, and Mumbai City
Datapoints were added onto the shapefile on QGIS as a Delimited Text Layer
Rainfall Map
Modelling the

## Slide 6
Rainfall in the MMR
The Rainfall map was modelled on QGIS using the Spatial Interpolation (IDW) Technique
Now, from the Interpolation Toolbox, I chose IDW Interpolation to add a Vector Layer for the interpolated data.
Pixel size of 0.001
Distance coefficient P of 2.0
Rainfall Map
Modelling the

## Slide 7
Rainfall in the MMR
The Rainfall map was modelled on QGIS using the Spatial Interpolation (IDW) Technique
To extract only the shapefile, I went to the Raster Tool and chose Extraction > Clip Raster by Mask Layer. This resulted in a crisp extraction of the interpolation. Then I modelled the intensity on a blue scale.
Rainfall Map
Modelling the
Mumbai City

## Slide 8
Elevation
  Most straightforward of all, we imported DEM data from the Bhuvan portal.
  From CartoDEM3 we take 4 tiles which are required to cover our ROI and then merge them in QGIS to get one raster layer.

## Slide 9
Elevation
  We then fill the sinks in it using Fill sinks (wang & liu).
  This gets rid of sudden changes in the DEM data which would have resulted in absurd slopes and would have thus hindered further analysis.

## Slide 10
Slope
  From the sink-filled DEM we get the slope map using the Slope tool in the Raster terrain analysis toolbox.
  The z-factor is a conversion factor that adjusts the units of measure for the vertical (or elevation) units when they are different from the horizontal coordinate (x,y) units of the input surface. It is the number of ground x,y units in one surface z-unit. If the vertical units are not corrected to the horizontal units, the results of surface tools will not be correct.
  Given that the latitude of Mumbai is about 19 degrees, we choose our Z-factor to be 0.00000956.
Source: https://pro.arcgis.com/en/pro-app/latest/tool-reference/spatial-analyst/applying-a-z-factor.htm

## Slide 11
  Rivers and streams are an important factor in flood risk assessment, because in a flood event these streams overflow and affect their banks.
  i.e., a region closer to a stream is at a greater flood risk
Rivers and Streams

## Slide 12
Distance from Rivers

## Slide 13
  Now from the Interpolation toolbox we use the Line density tool to create a Raster layer for drainage density.
  Search Radius: Defines the distance (in map units) around each cell where QGIS will search for line features to include in the density calculation.
  Pixel Size: The resolution of the output raster layer. Smaller pixel sizes give higher resolution but can increase processing time and file size.
Drainage Density
distance in degrees ≈ (distance in meters / 111,320) / cos(19°)
Approximate Values for 19° Latitude
  Search Radius: ~0.0047–0.0094 degrees
  Pixel Size: ~0.00009–0.00028 degrees

## Slide 14
For Search radius 1000m = 0.0094 and Pixel size of 300m = 0.0028 degrees

## Slide 15
  So here we see that there are many no-data values, which is bad because these areas will then have misleading calculations. Therefore we need to increase the search radius. We triple the radius to 3000m.
  For Search radius 3000m = 0.0282 and Pixel size of 100m = 0.0009 degrees we have the following:
distance in degrees ≈ (distance in meters / 111,320) / cos(19°)
Drainage Density

## Slide 16
  The topographic wetness index (TWI), which combines local upslope contributing area and slope, is commonly used to quantify topographic control on hydrological processes.
Topological Wetness Index (TWI)

## Slide 17
  Land use and land cover (LULC) is important for assessing flood risk because different types of land use impact the rate of infiltration, which can lead to increased runoff and a higher risk of flooding
LULC
  Water
  Trees
  Flooded Vegetation
  Built area
  Crops
  Bare ground
  Rangeland

## Slide 18
Flood Risk Modeling

## Slide 19
  Our final flood risk model works on a weighted average of the 7 layers:
    Slope
    Elevation
    Rainfall
    LULC
    TWI
    Distance from rivers
    Drainage density
  To decide these weights we did an extensive literature review.
  Some did cost/economic damage based analysis to decide on the weights (Waghwala Et al.)
  Others create a frequency ratio map (Samantha Et al.)
Weighing factors through literature and AHP

## Slide 20
Weighing factors through literature and AHP
  Now, based on these we perform an Analytical Hierarchy Process (AHP) (Saaty Et al.)
  AHP derives ratio scales from paired comparisons of criteria, and allows for some small inconsistencies in judgments. Inputs can be actual measurements, but also subjective opinions.
  Mathematically the method is based on the solution of an Eigenvalue problem. The results of the pair-wise comparisons are arranged in a matrix. The first (dominant) normalized right Eigen vector of the matrix gives the ratio scale (weighting), the Eigenvalue determines the consistency ratio.

## Slide 21
S. no. | Factor | % importance | Normalized weights
1 | Slope | 26.44 | 0.2644
2 | Elevation | 22.05 | 0.2205
3 | Rainfall | 17.69 | 0.1769
4 | LULC | 13.73 | 0.1373
5 | TWI | 8.10 | 0.0810
6 | Distance from river | 6.12 | 0.0612
7 | Drainage density | 5.87 | 0.0587

## Slide 22
Reclassifying layers in QGIS
Reclassified Elevation
Reclassified Slope
Reclassified TWI

## Slide 23
Reclassifying layers in QGIS
Reclassified Dist. from River
Reclassified Drainage Density
Reclassified LULC

## Slide 24
Reclassifying layers in QGIS
Reclassified Rainfall

## Slide 25
Final Raster Calculation
End Result
  Finally, weighing all the layers we get the overall flood risk over our ROI.
  (0.2644*"slope@1") + (0.2205*"elevation@1") + (0.1769*"rainfall_gaussian_filtered@1") + (0.1373*"lulc@1") + (0.0810*"twi@1") + (0.0612*"dist_riv@1") + (0.0587*"drain_dens@1")

## Slide 26
Validating Results
Mumbai City
Raw Data
Comparison with
Mumbai City received the most rainfall during the 2017 floods in the MMR
Raw Data from CHRS Data Portal

## Slide 27
1 . Mumbai City District
Flood Risk: Highest
Topographical Factors:
  Low Elevation and Flat Terrain: Mumbai City is predominantly low-lying which facilitates the accumulation of floodwaters
  Coastal Location: directly exposed to the Arabian Sea, making it susceptible to coastal flooding and storm surges
  Proximity to Major Water Bodies: increases the risk of riverine and pluvial flooding
Geographical Factors:
  Western Ghats Influence: cause orographic rainfall, enhancing precipitation intensity during the monsoon season
  Urban Geography: dense urban landscape with high-rise buildings and limited green spaces increases surface runoff
  Drainage Infrastructure: often inadequate to handle extreme rainfall events, especially during high tides
Topology/Geography

## Slide 28
1 . Mumbai City District
Flood Risk: Highest
Socioeconomic Factors:
    High Population Density: one of the highest population densities in the worl which increases flood risk due to pressure on drainage and infrastructure
    Economic Impact: Being a financial hub, flooding in Mumbai City leads to significant economic disruptions
    Limited Drainage Infrastructure: Older drainage systems struggle with extreme rainfall and tidal influences
    Health Risks and Poor Sanitation: mix with waste in densely populated slum areas, increasing disease risks post-flood
Socioeconomic Factors

## Slide 29
Resources and References
  Rainfall data: https://www.mahahp.gov.in/DisplayRainfall.aspx?data=Rainfall
  Shapefiles: https://github.com/IDFCInstitute/Cities_data/tree/master/Mumbai/Shapefiles/Municipal_Boundary
  LULC: https://livingatlas.arcgis.com/landcoverexplorer/
  River Network: https://www.hydrosheds.org/products/hydrorivers#downloads
  AHP: https://bpmsg.com/ahp/
  https://ijahp.org/index.php/IJAHP/article/view/590
  Other references:
  https://www.cityresource.in/data.html
  https://www.sciencedirect.com/science/article/abs/pii/S2212420918314493?via%3Dihub
  https://link.springer.com/article/10.1007/s13201-018-0710-1
  https://onlinelibrary.wiley.com/doi/10.1155/2021/6128609
  https://www.omdena.com/blog/flood-risk-assessment-using-ahp-and-ml-togo

## Slide 30
Thank You
For Your Attention